## Slide 1
C-Series
Basic Setup/ Operation Guide
Panasonic System Solution Asia Pacific
November 2016

## Slide 2
<NOTICE>
This document is supplementary to the operation manual.
The screens used in this document is taken from CJ-HDR416 with firmware version 3.200.ps00.0.r.20161102.
Depending on the firmware version, the screens may differ from the actual screens.

## Slide 3
HDD Installation
Display and Power Supply connection
Set Up Flow
SYSTEM Log in
General Setting
Camera Channel Encode Setting
Recording Schedule Setting
Recording Stream Setting
Network Setting
<Startup Wizard on DVR>
<Hardware Setup of DVR>
How to Manage Spare Camera Channel
<Important setting>
Camera Image Setting
<Additional Settings on DVR>
Access to DVR Web Console
Please make sure to configure important setting
Full HD: Resolution and FPS Settings

## Slide 4
Hardware Set up of DVR

## Slide 5
HDD Installation
①Loosen the screws of the upper cover and side pane
②Fix four screws in the HDD (Turn just three rounds).
③Place the HDD in accordance with the four holes in the bottom.
④Turn the device upside down and then turn the screws in firmly.
⑤Fix the HDD firmly.
⑥Connect the HDD cable and power cable.
⑦Put the cover in accordance with the clip and then place the upper cover back.
⑧Secure the screws in the rear panel and the side panel.
CJ-HDR216
CJ-HDR108
CJ-HDR104

## Slide 6
HDD Installation
① Loosen the screws of the upper cover.
② Line up the HDD to the four holes of the HDD bracket.
③ Use four screws to fix HDD.
④Unfasten the HDD power cable.
⑤Use the special data cable to connect the HDD and the SATA port
⑥Insert the HDD power cable. Close the chassis and fix the screws to secure firmly.
CJ-HDR416

## Slide 7
Connection Sample
CJ-HDR216
DC Power
(12V)
Audio In
RCA Port
Audio Out
RCA Port
Video In
BNC Port

## Slide 8
Connection Sample
CJ-HDR416
USB Mouse
(front or back)
AC Power
(100 V-240 V)
Video Out
BNC Port
Audio In
BNC Port
Video In
BNC Port

## Slide 9
Setup Wizard on DVR

## Slide 10
Startup Wizard(1/3)
Password : 12345
General Setting
Uncheck the button,
the setup wizard is cancelled next time
General Setting / Date & Time
Recommend to set NTP server
if internet is available
Change if necessary
Select local time
System Login
Startup Wizard

## Slide 11
Startup Wizard(2/3)
Camera Channel Encode Setting
<Step1>
Make sure you decide which camera to go to which channel
<Step2>
Example plug in the CH1 camera
into the Video In Port1
CH1
CH2
CH3
CH4
Port1
Port2
Port3
Port4
CBR is
recommended
2 Mbps is recommended for 720P resolution, 25fps recording.
2 Mbps is recommended for 1080P resolution, 15fps recording

## Slide 12
Startup Wizard(3/3)
24/7 recording is set as default
Recording Schedule Setting
End of Startup Wizard
Network Setting
Change if necessary
Main Stream schedule recording is set as default
Recording Stream Setting

## Slide 13
Important Setting
on DVR

## Slide 14
How to manage spare camera channel(1/3)
Turn off the Recording:
Go to MAIN MENU -> Setting -> STORAGE -> RECORD
[CAUTION]
If recording configuration of unused channel is left “ON”, it will consume recording HDD capacity and affect recording calculation.
Please make sure to turn off unused channels’ recording.
E.g.) When channel 1 & 2 are used, please turn off channel 3 to 16.

## Slide 15
How to manage spare camera channel(2/3)
Turn off the Video Loss detection:
Go to MAIN MENU -> Setting -> EVENT -> DETECT -> Video Loss
Select the Channel of unused camera and uncheck to disable the Video Loss Detection.
(E.g. When only Channel 1&2 is used for recording, please uncheck and disable the Video Loss Detection of Channel 3 to 16)
Before turn off Recording and Video Loss Detection.
After turn off Recording and Video Loss Detection, indication of Recording and Video Loss was remove.
Symptom 1:

## Slide 16
How to manage spare camera channel (3/3)
In EVENT-> ALARM STATUS
Before turn off Video Loss Detection, unused Channel Status was detected as abnormal video loss.
In EVENT-> ALARM STATUS
After turn off Video Loss Detection, unused Channel Status became normal.
In Playback and Search interface
Before turn off unused camera recording, unused camera showing recording data in Playback screens.
In Playback and Search interface
After turn off unused camera recording, unused camera showing no recording data in Playback screens as normal.
Symptom 2:
Symptom 3:

## Slide 17
Additional Setting
on DVR

## Slide 18
Full HD: Resolution and FPS Settings
When the Full HD camera is plugged into the DVR, the encode resolution message will be pop-out.
The content of the message is only available for firmware version 3.200.ps00.0.r.20161102 or later.

## Slide 19
Full HD: Resolution and FPS Settings
When the channel 1, 5, 9 or 13 are set to 16fps or more at 1080p, the other channels will be updated to 1080p 7fps or 720p 15fps. The message below will pop-up when “Encode” page is accessed.
For Example: When Channel 1 set to 16fps or more at 1080p, channel 2, 3 and 4 will be updated to 1080p 7fps or 720p 15fps.
The content of the message is only available for firmware version 3.200.ps00.0.r.20161102 or later.

## Slide 20
Full HD: Resolution and FPS Settings
Specifications

## Slide 21
Full HD: Resolution and FPS Settings
Specifications

## Slide 22
Camera Image Setting
Camera Image Setting
Video image adjustment
Click “CAMERA” for camera additional Setting
Change if necessary

## Slide 23
Access to DVR Web Console (1/2)
Connect the DVR to PC
Method 1 : Access to single DVR Web Console:
Connect the DVR to network switch
Method 2: Access to Multi DVR Web Console:
Connect the PC to network switch

## Slide 24
DVR Browser Access
Access to DVR Web Console(2/2)
Right Click
Start ConfigTool
The DVR is listed together with another devices connected the same LAN switch
Right Click, then select “Open Device Web”
ID : ADMIN
PWD : 12345
  Double Click

## Slide 25
Easy Operation

## Slide 26
Camera Preview (Live View) Interface
Preview control interface
Shortcut Menu
Right Click!
Real time Playback button : latest time playback
Digital Zoom button
Point cursor to
upper side
of the screen
Manual Record button : record on USB memory
Snapshot button
Playback and Search Mode
Window Split selection

## Slide 27
Playback and Search Interface
Video / Snapshot selection for playback
“Record” : Video select
“PIC” : Snapshot select
Window split mode(1/4/9/16)
Playback channel selection
Playback Control Panel
(Play/Pause/Play Backwards/
Fast Playback/Rewind/Slow Play)
Time Line Bar
Can change scale of time line
Display file list of the day
Calendar for playback
(Blue Highlighted date)
There is recorded data
(Yellow colored date)
Currently selected for
playback