## Slide 1
C-Series
DVR Operation Guide
Panasonic System Solution Asia Pacific
1st Jan 2016

## Slide 2
<NOTICE>
This document is supplementary to the operation manual.
The screens used in this document is taken from CJ-HDR416 with firmware version3.20.
Depending on the firmware version, the screens may differ from the actual screens.

## Slide 3
CONTENTS
Camera Preview(Live View)
Playback and Search
  Mark Playback
  File List
  Smart Search
Backup
  Screenshot
  Video Clipping
  File Backup

## Slide 4
Camera Preview (Live View) Interface
Preview control interface
Shortcut Menu
Right Click!
Real time Playback button : latest time playback
Digital Zoom button
Point cursor to
upper side
of the screen
Manual Record button : record on USB memory
Snapshot button
Playback and Search Mode
Window Split selection

## Slide 5
Playback and Search Interface
Video / Snapshot selection for playback
“Record” : Video select
“PIC” : Snapshot select
Window split mode(1/4/9/16)
Playback channel selection
Playback Control Pane
(Play/Pause/Play Backwards/
Fast Playback/Rewind/Slow Play)
Time Line Bar
Can change scale of time line
Display file list of the day
Calendar for playback
(Blue Highlighted date)
There is recorded data
(Yellow colored date)
Currently selected for
playback

## Slide 6
Playback and Search - Mark Playback
1. Click Bookmark button to add mark
2. Put Name to the Mark Name
3. Click Mark File list button
to see the list of marked files
(Note: this button will work
only in single channel mode)

## Slide 7
Playback and Search - File List
1. Click File List button
3. Click File Lock button after selected a file in the list
Locked files will not be overwritten
4. Click Search Locked File button
to see the list of locked files
2.
-Check Start time to select
-Double Click to playback
[NOTE]
C series DVR stores recorded video as file.

## Slide 8
Playback and Search – Smart Search
1. Preparation : Go to SETTING > EVENT > DETECT > Motion Detect
4. Select search area with mouse drag
5. Click Motion Search Button
2. Check Enable
3. Click Motion Search button
-Smart Search is now working
-Click again Motion Search button to stop smart search playback

## Slide 9
Backup – Screenshot
1. Click “Full Screen” button
2. Click “Screenshot” button
Precondition
Insert USB memory to USB port on DVR
[CAUTION]
USB memory need to be formatted as FAT32
[NOTE]
Screenshot is saved in USB memory .
Screenshot image is saved as JPEG file.
Sample Screenshot
3. Click “Start” to save the screenshot

## Slide 10
Backup - Video Clipping
3. To select Start Time, click and drag the marker that appears at the left most of timeline bar
4. To select End Time, click and drag the marker that appears at the right most of timeline bar
2. Click Video Clip button to decide start time & end time of the video
Precondition
Insert USB memory to USB port on DVR
6. Check the clipped file for backup, then click Backup
1.Click the channel screen to clip the video
[CAUTION]
USB memory need to be formatted as FAT32
5. Push Save button,
then back up window is pop up

## Slide 11
Backup - File Backup
2. Specify time period and click “Add” button
3. Check the required files and click “Start” button to backup
This window pop up after insertion of USB memory
to USB port on DVR
1. Click file backup