## Slide 1
Panasonic C-Series
27th Apr 2021
Panasonic System Solutions Asia Pacific

## Slide 2
What is C-Series?
Clarity
2. Connectivity
3. Convenience

## Slide 3
FHD Analog
Camera

## Slide 4
Model Number of C-series Camera
 | TYPE |  |  | Model Number
HD | IR Dome Camera | Varifocal | 2.7-13.5mm | CV-CFW101AL
 |  | Fixed | 3.6mm | CV-CFW103AL
 |  | Fixed | 3.6mm | CV-CFN103AL (Indoor)
 | IR Box Camera | Varifocal | 2.7-13.5mm | CV-CPW101AL
 |  | Fixed | 3.6mm | CV-CPW103AL
FHD | IR Dome Camera | Varifocal | 2.7-12mm | CV-CFW201L, CV-CFW201AL
 |  | Fixed | 3.6mm | CV-CFW203L, CV-CFW203AL
 |  | Fixed | 3.6mm | CV-CFN203L (Indoor)
 | IR Box Camera | Varifocal | 2.7-12mm | CV-CPW201L, CV-CPW201AL
 |  | Fixed | 3.6mm | CV-CPW203L
 |  | Fixed | 3.6mm | CV-CPW203L, CV-CPW203AL

## Slide 5
Model Number of C-series DVR
Category | Type |  | Model | 
Recorder | DVR | 4CH |  | CJ-HDR104, CJ-HDR104A
 |  | 8CH |  | CJ-HDR108, CJ-HDR108A
 |  | 16CH |  | CJ-HDR216, CJ-HDR216A
 |  | 16CH |  | CJ-HDR416, CJ-HDR416A
Recorder | DVR | 4CH |  | CJ-HDR104B
 |  | 8CH |  | CJ-HDR108B

## Slide 6: C-Series Model Number (Camera)
C
V
-
C
F
W
1
0
1
L
Category
Form
Factor 1
Form
Factor 2
Resolution
Focal length
F: Dome
P: Box
W: Weather
N: Indoor
1: 720P / 1.0MP
2: 1080P / 2.0MP
1: Varifocal
3: 3.6mm
L: IR LED
IR LED
A
A ,B,C……
Hardware
version

## Slide 7: C-Series Model Number (Recorder)
C
J
-
H
D
R
1
0
4
Category
SATA port for HDD
Channel
1: 1 SATA Port
2: 2 SATA Port
4: 4 SATA port
04: 4 Channel
08: 8 Channel
16: 16 Channel
A
A ,B,C……
Hardware
version

## Slide 8
Varifocal IR Dome HD Analog Camera
1080p IP66 IR HD Analog Camera
Model number :
CV-CFW201AL (PAL/NTSC)
Focal Length: 2.7mm - 12mm (Motorized vari-focal)
Overview
1/2.7" 2.0 Mega Pixels CMOS.
1080p@25fps(PAL) /30fps (NTSC).
75-3 coaxial cable (Belden 9259 or equivalent) transmission up to 800m.
ICR for day time and night time operation.
Auto exposure, auto white balance, auto electronic shutter and auto gain function.
Motorized adjustment of lens zoom and focus.
DC12V power supply.
IP66 compliance.

## Slide 9
Fixed IR Dome HD Analog Camera
1080p IP66 IR HD Analog Camera
Model number :
CV-CFW203AL (PAL/NTSC)
Focal Length: 3.6mm
Overview
1/2.7" 2.0 Mega Pixels CMOS.
1080p@25fps(PAL) /30fps (NTSC).
75-3 coaxial cable (Belden 9259 or equivalent) transmission up to 800m.
ICR for day time and night time operation.
Auto exposure, auto white balance, auto electronic shutter and auto gain function.
Fixed Focal Len.
DC12V power supply.
IP66 compliance.

## Slide 10
Varifocal IR Dome HD Analog Camera
1080p IP66 IR HD Analog Camera
Model number :
CV-CPW201AL (PAL/NTSC)
Focal Length: 2.7mm - 12mm (Motorized vari-focal)
Overview
1/2.7" 2.0 Mega Pixels CMOS.
1080p@25fps(PAL) /30fps (NTSC).
75-3 coaxial cable(Belden 9259 or equivalent) transmission up to 800m.
ICR for day time and night time operation.
Auto exposure, auto white balance, auto electronic shutter and auto gain function.
Motorized adjustment of lens zoom and focus.
DC12V power supply.
IP66 compliance.

## Slide 11
Fixed IR Dome HD Analog Camera
1080p IP66 IR HD Analog Camera
Model number :
CV-CPW203AL (PAL/NTSC)
Focal Length: 3.6mm
Overview
1/2.7" 2.0 Mega Pixels CMOS.
1080p@25fps(PAL) /30fps (NTSC).
75-3 coaxial cable(Belden 9259 or equivalent) transmission up to 800m.
ICR for day time and night time operation.
Auto exposure, auto white balance, auto electronic shutter and auto gain function.
Fixed Focal Len.
DC12V power supply.
IP66 compliance.

## Slide 12
Specifications for FHD Camera
 | Dome |  | Box | 
 | Vari-focal | Fixed | Vari-focal | Fixed
Model Number | CV-CFW201AL | CV-CFW203AL | CV-CPW201AL | CV-CPW203AL
Camera |  |  |  | 
Image Sensor | 1/2.7" 2.0 Mega Pixels CMOS |  |  | 
Effective Pixels | 1920 (H) x 1080 (V) |  |  | 
Min Illumination | 0.02Lux/F1.7 30IRE, 0Lux/IR on | 0.02Lux/F1.9 30IRE, 0Lux/IR on | 0.02Lux/F1.7 30IRE, 0Lux/IR on | 0.02Lux/F1.9 30IRE, 0Lux/IR on
Video Frame Rate | 25fps (PAL), 30fps (NTSC) |  |  | 
Day & Night | Auto(ICR) / Color / B/W |  |  | 
Max IR Distance | 60m | 30m | 60m | 40m
Digital Noise Reduction | 2D |  |  | 
White Balance, AGC, BLC | Auto |  |  | 
Lens |  |  |  | 
Focal Length | 2.7 ~12mm | 3.6 mm | 2.7 ~12mm | 3.6 mm
Angular Field of View | H: 33°~102° V: 19°~53° | H: 84° V:45° | H: 33°~102° V: 19°~53° | H: 84° V:45
General |  |  |  | 
Weatherproof | IP66 | IP66 | IP66 | IP66

## Slide 13
DVR

## Slide 14
4/8ch HD DVR (1 SATA HDD)
Overview
4ch (CJ-HDR104B) / 8ch (CJ-HDR108B) with 720P/1080P real-time recording playback and live view
H.264 and H.265 video compression
HDMI / VGA simultaneous video output
Support 1 SATA HDD up to 6TB for CJ-HDR104B
Support 1 SATA HDD up to 10TB for CJ-HDR108B
2 ports of USB2.0
Digital Zoom during Live & Playback
iPhone, iPad & Android
Video Motion Detection (VMD)
Daily Health Report
Model number : CJ-HDR104B (4ch) / CJ-HDR108B (8ch)

## Slide 15
16ch HD DVR (2 SATA HDD)
Overview
16 channel with 720p real-time recording playback and live view
H.264 video encode
1/4/9/16 channel synchronous real time playback
HDMI / VGA simultaneous video output
Support 2 SATA HDDs up to 12 TB, 2 USB
Digital Zoom in Live & Playback
iPhone, iPad & Android
Model number : CJ-HDR216A (16ch)

## Slide 16
16ch HD DVR (4 SATA HDD)
Model number : CJ-HDR416A (16ch)
Overview
16 channel with 720p real-time recording playback and live view
H.264 video encode
1/4/9/16 channel synchronous real time playback
HDMI / VGA / BNC(TV) simultaneous video output
Support 4 SATA HDDs up to 24TB, 3 USB
Digital Zoom in Live & Playback
iPhone, iPad & Android

## Slide 17
Specifications (DVR A-model)
Model Number |  |  | CJ-HDR104B | CJ-HDR108B | CJ-HDR216A | CJ-HDR416A
Video / Audio Interface | Video Input |  | 4 CH, BNC | 8 CH, BNC | 16 CH, BNC | 16 CH, BNC
 | Type | HDCVI | 1080P/720P |  |  | 
 |  | Analog | NTSC/PAL |  |  | 
 | Video Output |  | 1 HDMI, 1 VGA |  |  | 2 HDMI, 1 VGA, 1 BNC
 | Audio Input |  | 1 CH, RCA |  |  | 4 CH, BNC
 | Audio Output |  | 1 CH, RCA |  |  | 1 CH, BNC
Display | Multiscreen Mode |  | 1/4 | 1/4/8/9 | 1/4/8/9/16 | 1/4/8/9/16
Video / Audio Format | Video/Audio Compression |  | H.264, H.265 / G.711a | H.264, H.265 / G.711a | H.264 / G.711a | H.264 / G.711a
 | Record Rate | Main Stream | 1080P/720P/960H/D1/CIF/(1~25/30fps) |  |  | 
 |  | Sub Stream | D1/CIF/ (1~15fps) |  |  | 
Alarm / Event | Alarm Input |  | - | - | - | 16 CH
 | Relay Output |  | - | - | - | 6 CH
 | Trigger Events |  | Recording, PTZ, Tour, Email, FTP, Snapshot, Buzzer, Show Message, Alarm Upload and Log * |  |  | 
Playback & Backup | Sync Playback |  | 1/4 | 1/4/9 | 1/4/9/16 | 1/4/9/16
Network | Mobile Device |  | iPhone, iPad, Android |  |  | 
HDD | Unit |  | 1 SATA Port (up to 6 TB) | 1 SATA Port (up to 10 TB) | 2 SATA Port (up to 8 TB for each disk) | 4 SATA Port (up to 8 TB for each disk)
External Interface | USB Interface |  | 2 Port (1 rear), USB 2.0 |  | 2 Port (1 rear), 1 USB 2.0, 1 USB 3.0 | 3 Port, USB 2.0
For CJ-HDR416 only
Remark:
- For channel 1 and channel 5 (CJ-HDR108A only), the change of the frame rate to 16fps or more at 1080P and above, will update the frame rate settings of other channels to 15fps.
- Recommended to schedule a weekly reboot.

## Slide 18
Recording calculator available
Recording volume calculator Ver3.00
You can download the latest calculator from
http://security.panasonic.com/library/c-series/
Reference bitrate and range of selectable bitrate are shown on “Bitrate table” sheet in the calculator.

## Slide 19
C-series & Analog connectivity & Limitations
*1 : In theory, 3rd Party HD-CVI devices work with Panasonic C-Series. However, when using 3rd party devices, prior testing is recommended.
*2 : It depends on 3rd party recorder's specifications.
 |  | Camera |  | 
 |  | Panasonic C-Series | Analog | C-series & Analog mix
DVR | Panasonic C-Series | OK | OK | OK
 | Analog (HD716/X-Plus/3rd party) | NO | OK | NO
 |  | Camera |  | 
 |  | Panasonic C-series | 3rd party HD-CVI | 3rd party others (HD-TVI, AHD, etc.)
DVR | Panasonic C-Series | OK | OK (*1) | NO
 | 3rd party HD-CVI | OK (*1) | OK (*1) | NO
 | 3rd party others (HD-TVI, AHD, etc.) | NO | NO | - (*2)
C-Series with Analog camera/recorder
C-Series with 3rd party FHD analog camera/ recorder
<Note>
The above tables refer to image connectivity. PTZ operation are not taken into account.
PTZ operation (Panasonic Analog PTZ (WV-CW590 & CS580) and C-series recorder) will be evaluated.